## Slide 1
The War Lords Trilogy
Chapter 2: Technology Age
E1200-AP

## Slide 2
Lab 1: Local Area Network Connectivity | 
Objectives: | To provide connectivity of devices within a LAN. Validation of connectivity: Using the ping utility to get acknowledgment from your Wireless AP. Using the ping utility on your laptops to successfully get acknowledgments from all other laptops connected to the same LAN. (BONUS) Using the LAN Messenger app to chat with users on the same LAN
Pre-lab setup/research | Turn off the firewall function on your laptop. (based on your OS) Find out what is the procedure to manually enter IP address on your laptop (based on your OS) (BONUS) Download the LAN Messenger app. http://lanmsngr.sourceforge.net/downloads.php
Resources: | 1 x Linksys E1200-AP per Group (Wireless Access Point) Laptops
 | Tasks | References
1 | On your laptop, scan for all the SSIDs broadcasted by the Wireless Access Points in the room. Connect to the SSID assigned to your Group. This process is known as AP association phase. Upon successful association of laptop with AP observed the properties of your wireless connection How does your laptop identify itself on the network ? ________________________________________________________________________ Will you be able to communicate with the other laptops in your group ? ________________________________________________________________________ ________________________________________________________________________ | Refer to Appendix 1: Network Diagram Refer to the notes in Appendix 2: 802.11 Association process On Android OS: PingTools Network Utilities from StreamSoft

## Slide 3
 | Tasks | References
2 | Discuss with your group members so that every laptop will be assigned a unique IP address from the range given to your group. Assigned IP address: _______________________ Configure the IP Address and subnet mask on your laptop. Leave the rest of the configuration as default/empty. On Windows, open a command prompt windows, On Mac OS, open a terminal app. To verify that the IP address is set enter the following command: Windows: ipconfig Mac OS : ifconfig To test connectivity, type the following command, where <destination IP address> is the IP address of another laptop in your group. (make sure they have successfully configured their IP address) ping <destination IP address> For a successful connectivity, you will get a response similar to “ Reply from ...” (BONUS) Install the LAN Messenger app and launch the app. You should be able to detect the users in your group that have the LAN Messenger installed and exchange messages with them. (Similar to WhatsApp but the contacts are the users in the same LAN) How does the app detect the laptop users that are on the same LAN. __________________________________________________________________________ To complete the lab successfully, all the laptops in your group should be able to connect to each other. | Refer to Appendix 1: Network Diagram LAN Messenger App settings -set Tools\preference\network -> add 255.255.255.255, 192.168.X.255 (X=Group No) - set Tools\preferencesAccounts\Reresh contact list 5 secs

## Slide 4
E1200-AP
SSID | GRP10
IP address range: | 192.168.10.100 to 192.168.10.150
Subnet Mask: | 255.255.255.0
E1200-AP
E1200-AP
SSID | GRP20
IP address range: | 192.168.20.100 to 192.168.20.150
Subnet Mask: | 255.255.255.0
SSID | GRP30
IP address range: | 192.168.30.100 to 192.168.30.150
Subnet Mask: | 255.255.255.0
Appendix 1: Network Diagram
Jial Le
Jing Jie
Naren

## Slide 5
E1200-AP
E1200-AP
E1200-AP